## Slide 1: Status of CEPC xxxxxxxx Readout Electronics

## Slide 2: SDHCAL based on GEM
GEM with self-stretching techniques
  Advantages：
    1. Easy assembling
    2. Uniform gas flow
    3. Detachable
    4. No dead area inside the active area
Detector and readout plane with 1cmx1cm size

## Slide 3: Readout Electronics Design
FEB with MICROROC
  Single board with 256 channels
  Connected via flexible plate
DIF
  Multiple readout interfaces such as DTCC, SFP, Ethernet and USB

## Slide 4: Cosmic-Ray Test
Use two PMT for coincidence detection

## Slide 5: Cosmic-Ray Test
Scan the gain of detector to obtain the efficiency and multiplicity
Scan the threshold under thes
Detection efficiency and multiplicity vary with voltage
Detection efficiency and multiplicity vary with threshold

## Slide 6: Next Step
A readout plane with embedded front-end electronics is designed
Blind buried via technique is used to ensure the signal integrity and gas tightness

## Slide 7: Back Up

## Slide 8: Laboratory Test
An external ADC is applied to measure the X-Ray energy spectrum
The detector gain uniform is obtained by the spectrum